## Slide 1
01 / 11
📡
FINAL YEAR PROJECT PRESENTATION
PeerLink
An offline, internet-free peer-to-peer messaging system using an ESP32 microcontroller as a portable Wi-Fi relay hub for Android devices.
Android
ESP32
Jetpack
UDP Mesh

## Slide 2
02 / 11
MOTIVATION
The Problem
🌐
Internet Dependency
All popular messaging apps rely on cloud servers and active internet connectivity to exchange messages.
🚫
Dead Zones
Remote areas, disaster zones, underground venues, and events often have no cellular signal or Wi-Fi infrastructure.
🔒
Privacy & Surveillance
Server-based messaging exposes messages to third-party cloud providers, creating privacy and security concerns.
💡 The Need: A simple, infrastructure-free communication method that works with just a small device and smartphones.

## Slide 3
03 / 11
SOLUTION
Introducing PeerLink
PeerLink transforms an ESP32 microcontroller into a portable Wi-Fi relay hub. Nearby Android phones connect to it and can chat with each other — completely offline, no SIM card, no internet, no server. • Works anywhere — even in remote areas • No registration, no accounts, no cloud • ESP32 costs under ₹400 and runs on a phone charger • End-to-end local network
📡
ESP32 Acts As:
• Wi-Fi Access Point (hotspot) • UDP packet relay / router • Client registry & tracker • Presence broadcaster

## Slide 4
04 / 11
SYSTEM DESIGN
Architecture Overview
📱
Android App
Sender
→
⚡
WifiNetworkSpecifier
Auto-connects
→
🔧
ESP32 Relay
Routes port 8888
→
📲
Android App
Receiver
EspConnector
Auto-joins PeerLink Wi-Fi using APIs
UdpChat
Sends/receives JSON packets on UDP 8888
MeshService
Android Foreground Service orchestration
Room DB
Persists chat history locally

## Slide 5
05 / 11
HARDWARE LAYER
ESP32 Relay Firmware
• Wi-Fi AP Mode — Broadcasts SSID PeerLink_XXXX • UDP Server on port 8888 — Listens and routes • Client Registry — Tracks all connected devices • Presence Broadcast — Announces relay every 2s • Client Timeout — Removes inactive devices (30s) • LED Indicator — GPIO 2 blinks on activity
// Message routing logic (simplified) if (type == "chat") { if (to == "BROADCAST") { for (auto &[id, info] : clients) forwardPacket(json, info.ip); } else { forwardPacket(json, clients[to].ip); } } else if (type == "get_clients") { sendClientList(senderIP); }
Arduino C++
ArduinoJson

## Slide 6
06 / 11
ANDROID LAYER
Android Application
🔌
EspConnector
Uses Android's WifiNetworkSpecifier API to connect to hotspot networks via Kotlin callbackFlow.
📦
UdpChat
Manages DatagramSocket on port 8888 for UdpPacket objects. Uses Coroutines & MutableSharedFlow.
⚙️
MeshService
Foreground Service staying alive in background. Orchestrates DB and state flows.
🗄️
Room Database
Persists MessageEntity records locally. UI observes via a Flow<List<MessageEntity>>.

## Slide 7
07 / 11
USER INTERFACE
App Screen Flow
✨
Splash Screen
Brand intro
→
🔑
Permission
Wi-Fi, Location
→
📡
Discovery
Connecting
→
👥
Device List
Shows peers
→
💬
Chat Screen
Messaging
Jetpack Compose
Declarative UI with Material 3, reactive state.
Navigation
Type-safe navigation with NavHost.
Dark Theme
Black background with white bubbles.

## Slide 8
08 / 11
DEEP DIVE
Message Data Flow
// 1. User taps Send → ViewModel → MeshService fun sendMessage(toPeerId: String, content: String) { val packet = UdpPacket(type="chat", from=myDeviceId, to=toPeerId, payload=content) database.messageDao().insertMessage(localMsg) // Save locally first udpChat.sendMessage(packet) // Send over UDP → ESP32 router } // 2. ESP32 receives packet → looks up target device IP → forwards // 3. Receiver's UdpChat emits via SharedFlow → MeshService handles when (packet.type) { "chat" -> database.messageDao().insertMessage(incomingMsg) "clients_list" -> _serviceState.update { it.copy(peers = parsedPeers) } } // 4. Room DB change → Flow emits → Compose UI auto-recomposes
Coroutines
StateFlow
Room Flow

## Slide 9
09 / 11
TECHNOLOGY
Technology Stack
📱
Android / Kotlin
Jetpack Compose · Navigation · ViewModel · Room DB · Foreground Services
⚡
Embedded / C++
ESP32 Arduino SDK · WiFi.h · WiFiUdp.h · ArduinoJson
🌐
Networking
WifiNetworkSpecifier API · UDP Datagrams · Port 8888 · Broadcast routing
0
Internet Required
<₹400
Hardware Cost
8888
UDP Port
2s
Broadcast Interval

## Slide 10
10 / 11
IMPACT & ROADMAP
Use Cases & Future Scope
🎯 Real-World Use Cases • Disaster Relief — Communication when towers are down • Remote Expeditions — Trekking, camping, mountaineering • Event Management — Large venues with poor connectivity • Underground Facilities — Mines, bunkers, basements • Campus / Office — Private local-only communication
🚀 Future Enhancements • Multi-hop mesh relay (ESP32 to ESP32 chaining) • End-to-end message encryption (AES/RSA) • File / image transfer support • Group chat & broadcast channels • iOS client application

## Slide 11
11 / 11
📡
END OF PRESENTATION
Thank You
PeerLink — Connecting People, Offline.
📱
Android (Kotlin)
⚙️
ESP32 Firmware
💬
Offline Mesh
Built with Kotlin · Jetpack Compose · ESP32 Arduino · UDP Networking